CHECKLIST

NOTE ON CHECKLISTS

A normal checklist is provided for use in flight. This checklist covers items that are of vital importance to the safety of the flight.

When completing a checklist it is assumed the pilot is familiar with the full operating procedures in the sections following the normal checklist and outlined in the aircraft POH section 4. The checklist is completed after normal flows as a cross check to ensure critical items are set correctly.

Expanded procedures for normal, non-normal, and emergency operations are provided on the reverse side. These should be used for training aids during type ratings and for personal reference.

As model differences frequently occur, the manufactures handbook for the aircraft you are flying should be referenced to and this checklist must be modified accordingly prior to any use operation!

Speeds and performance figures provided here are an average for the more common C182 models and rounded up to the nearest 5kts.

HAPPY FLIYING

RED SKY CHECKLISTS
Cessna 182

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW condition.
VR	55 KIAS
VX – Best Angle of Climb	65 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Normal approach	70-80 KIAS
Vref	65 KIAS
VA – Maneuvering Speed	111 KIAS

Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS

VNO – Top of Green Arc	140 KIAS
VNE – Red Line (Never Exceed)	167 KIAS

VSO – Stall landing configuration	52 KIAS
VS – Stall Clean	58 KIAS

VFE – Max. Flap Extension 10-40º	110 KIAS
VFE – Max. Flap Extension 0-10 º	140 KIAS

EMERGENCY OPERATION
Best glide Speed	70 KIAS
Precautionary
Slow safe Cruise	90-105 KIAS
Approach (flaps up)	70 KIAS
Approach (flaps full)	65 KIAS
Ditching	65 KIAS
Engine failure after takeoff	70 KIAS
Engine Failure in flight flap up	70 KIAS
Engine Failure in flight flap down	65 KIAS

PERFORMANCE

Before Leaving Home
“I'M SAFE”
Self Check
Illness
Medication	No
Stress	No
Alcohol in last 8 hrs	No
Feeling OK	Yes
Eaten	Yes

Flight Equipment Check

Crew Licenses
Strainer, Dipstick, Leatherman
Current Charts
Airport Guide/Airfield Charts
Custom Checklists
Text Books
Flight Plans
Weather Reports
Flight Computer, Plotter Calculator,
Pencils, Clipboard
Time Piece
Flashlights, Batteries, Bulbs
Cell Phone (Charged)
Spare Glasses, Sun Glasses

SPCRM

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics, Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Pre Run Up
Parking Brake	Set
Fuel Selector	Both
Engine Instruments	Green
Cowls.....	Open

NORMAL CHECKLIST

Loading
Maximum TO/Ldg Weight	2800lbs
Standard Empty Weight	1600lbs
Useful Load	1200lbs
Operating performance
Fuel Capacity (useable)
Standard	56gals
Long Range	75gals
Fuel Consumption
75%@2500ft	55lt /hr
75%@7500ft	45 /hr
Planning	60 /hr
Plan Cruise speed	125KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Radio Frequencies
Emergency Frequencies	121.5/243
All Africa TIBA	126.9
Uncontrolled/Unmanned:	124.8
Training Areas:	124.4

Light Signals
Signal	On Ground	In Flight
Green Steady	Takeoff	Land
Green Flashing	Taxi	Return to land
Red Steady	Stop	Give way
Red Flashing	Clear runway	Do not land
White Flashing	Return to ramp	--
Red/Green alternating	WARNING – USE CAUTION

PERFORMANCE

Run Up
Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check
Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Governor	Full fine
Flight Controls	Free and Correct
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Runup....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Perform
Line Up
Area.......	Clear
Landing light, strobes	On
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Area.......	Clear
Windsock.......	Check
Engine Parameters	Green

NORMAL CHECKLIST

After Takeoff (above 1000' AGL
Brakes....	Check
Undercarriage	Retracted
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d
Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down & Locked
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked
Propeller Pitch	Full fine

NORMAL CHECKLIST

Short field take-off
Wing Flaps	20 deg
Brakes	APPLY
Power	Maximum
Mixture	Set for Field Elevation
Brakes	RELEASE
Elevator Control	Slightly Tail Low
Lift Nose	60KIAS
Maintain	65KIAS
Until clear of Obstacles

Accelerate	80KIAS
Wing Flaps (above70KIAS)	RETRACT
Power	Set for climb

Note: Do not reduce power until wing flaps have been retracted.s
Soft field take-off
Wing Flaps	Maximum for field
Line up	Do not stop rolling
Takeoff roll	Nose high
Liftoff	Minimum speed
Accelerate	65KIAS
Until clear of Obstacles, continue with Short Field Procedure

Maximum Performance Climb
Wing Flaps	Up
Power	Maximum Climb
Pitch	Maximum Continuous
Note: for an after takeoff climb or in an emergency full power may be used ensure time limits are not exceeded for normal operations
Mixture	Set for Field Elevation
Airspeed	Vysl 80 KIAS (sea level)
Vy10,000 75 KIAS (10,000ft)
Cowl Flaps	Open
Note: Vy will provide maximum rate of climb, when performance is limiting such that less than 200fpm is achieved, the reduction to best angle of climb may result in zero or negative rate of climb.

ABNORMAL PROCEDURES

Abnormal Maneuvers

HASELL
Complete prior to conducting stalls, spins and approved aerobatic maneuvers
Height	Sufficient for recovery
Above 3000ft AG

Airframe	Limitations Reviewed
Configuration Reviewed

Security	Seatbelts/Passengers/Load
Engine	Temperatures/Pressures
Power/Pitch Mixture Checked
Location	Not over built up areas,
airfields or controlled airspace High Terrain
Within proximity of suitable landing areas
Lookout	Complete a lookout turn

ABNORMAL PROCEDURES

Engine failure
TAKEOFF
NOTE: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist.
Throttle	IDLE
Brakes	Apply
Flaps	UP
Mixture	IDLE cut-off
Ignition	OFF
Master switch	OFF
AFTER TAKEOFF
Airspeed	70 KIAS Flaps Up
65 KIAS Flaps Down
Mixture	Idle Cut-off
Fuel shutoff valve	OFF
Ignition	OFF
Flaps	as required
Master switch	OFF
DURING FLIGHT
IMMEDIATE ACTIONS
Airspeed	70KIAS
Carb Heat	ON
Field	Select
Approach	Plan
FINDING
Carb Heat	ON
Primer	IN & Locked
Fuel Shutoff valve	ON
Mixture	RICH
Ignition	BOTH (or START)
COMMUNICATE
Mayday	Transmit on Active or 121.5
Transponder	7700
Passengers	Brief
SECURE
Mixture	cutoff
Fuel shutoff valve	off
Ignition	off
FINAL
Flaps	as required
Master switch	Off
Doors	unlatch
Touchdown	tail low
Note: It is recommended that engine failure during fight procedures be committed to memory

EMERGENCY PROCEDURES

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached

NORMAL CHECKLIST

Short field landing
Flaps	Full
Airspeed	65kts
Touchdown Positive, Main Wheels First
Nose Wheel	Lower
Braking	Maximum Steady Braking
Flaps	Retract
Soft field landing
Flaps	Full
Airspeed	65kts
Touchdown,	Softly Main Wheels First
Nose Wheel	Lower gently
Elevator	Full up
Braking	Gently, minimum required
Flaps	Leave down until clear of rwy
Crosswind take-off
Wing Flaps	Minimum for field
Takeoff roll	Ailerons Into wind
Liftoff	Ailerons Neutra
Liftoff	Vr nml+
After takeoff	Crab into wind for drift

Crosswind landing
Wing Flaps	minimum for field length
(and as required by strength of wind)
Approach	crab into wind

Touchdown	Nose straight, into wind wheel first
After landing	Ailerons into wind
Note: maximum demonstrated crosswind
Go-around
Mixture/Pitch/Throttle	Forward
Wing Flaps	Retract to Takeoff
Brakes	APPLY

(after obstacles are cleared and above Vx )
 Wing Flaps	RETRACT
Power	Set for climb

Note: Do not reduce power until wing flaps and landing gear have been retracted.
ABNORMAL PROCEDURES

Engine Fire
during start
Starter	Crank
To draw away flames, If Engine Starts:
Power	1700rpm
For a few minutes until flames appear to be extinguished, or if engine does not start:
Mixture	IDLE cut-off
Ignition	OFF
Master	OFF
Inspect damage
during flight
Mixture	IDLE cut-off
Fuel	OFF
Master	OFF
Cabin Air	OFF
Sideslip	Initiate if required
Proceed with Engine Failure in Flight Actions

Cabin Fire
On the Ground
Master Switch	OFF
Cabin Vents/Air/Heat	Closed
Fire Extinguisher	Activate
Cabin Vents/Windhws	Open

During flight
Follow Above Procedure, Once Fire is extinguished:
Electrics/Avionics	Off
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

Electrical Fire
Unknown Source
Master Switch	OFF
Avionics and Electrics	OFF
Circuit Brekers	PULL
If Smoke Ceases:
Master Switch	ON
Essential Electrical/Avionics	On, One at a time

EMERGENCY PROCEDURES
Electrical failure
Load	Verify
Reduce to minimum
Alternator	OFF
Alternator CB	Trip&Reset
Alternator	ON
If no Power
Alternator	OFF

PLAN To land at nearest suitable airfield,
Conserve Battery as much as possible,
All non essential electrics off, if necessary Inform ATC and turn master off until approaching circuit.
Be prepared for implications of electrical failures on systems(flaps/gear)

Electrical overload
Load	verify
Reduce to minimum
Alternator	OFF
Alternator CB	Trip&Reset
Alternator	ON
Load	OK?

If Not:
Master	OFF
Master	ON

IF LOAD still not does not return to normal land at nearest suitable airfield.

Carburetor Icing
Carb Heat	Fully ON
Mixture	Adjust
Once icing/roughness has cleared;
Carb Heat	Cold
Mixture	Reset
Engine Roughness
Magnetos	Check
Mixture	Adjust
Temperatures/Pressures	Check
If roughness continues, plan to land at nerest suitable airfield.

EMERGENCY PROCEDURES

Cockpit Inspection
Aircraft documents	Check
Pilot's Operating Handbook
Aircraft Weight & Balance records
Certificate Of Airworthiness a
Certificate of Registration
Maintenance Release
Aircraft Radio license
Flight Folio
Control wheel lock	Remove
Hobbs/Tach	Check/Record
Ignition	Off
Avionics Master (if fitted)	Off
Master Switch	On
Fuel quantity indicators	Check
Flaps	Down
Lights	On and Check (if Req'd)
Pitot heat	On and Check (if Req'd)
Master Switch	Off
Fuel shutoff valve	On
Brakes	Test and Set
Gust Locks	Remove
Covers and tie downs	Remove

NOTE: PROPELLERS SHOULD BE TREATED AS LIVE AT ALL TIMES REGARDLES OF THE POSITION OF ENGINE CONTROL SWITCHES

Fuselage and Empenage
Baggage Door	Check and Lock
Rivets	Check, Secure
Nav Light	Check, Secure
Elevator	Free movement, Secure
Elevator Trim	Check, Secure
Balance weights	Secure
Lock wires	Check, Secure
Radio antennas	Check, Secure
Balance weights	Secure
Rudder	Free, Secure
Beacon	Check, Secure

Before starting engine
Chocks	Removed
Preflight	Complete
Seats/Seat Belts	Adjusted & Locked
Brakes	Set and Hold
Cowl Flaps	Open
Fuel Selector	Fullest Tank
Lights	OFF
Circuit Breakers	Check IN
Clock	Set
Altimeter	Set
Avionics	OFF
Electrical Equipment	OFF
Beacon	ON

Normal Start
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter Open
Carburetor Heat..	Cold
Magnetos	Both
Prime.....	1-3 as req’d
Rotating Beacon....	On
Master Switch...	On
Prop Area.......	Clear

START Accomplish:
Ignition Switch....	Engage
As engine fires:
Throttle........	....Minimum
Oil Pressure	Rising within 30s

Flooded Start
Mixture....	Cut-Off
Power......	Full
Prop Area.......	Clear

START Accomplish:
Ignition Switch....	Engage
As engine fires:
Mixture	Rich
Throttle........	....Minimum rpm
Oil Pressure Rising..	Rising within 30s

Before Takeoff
(“Too Many Pilots Fly In Heaven Early”
Test Controls	Free & Correct
Trim	Set for T/O
Throttle friction lock	Set
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Governor	Full fine
Primer	Locked
Pumps	As required
Flight Controls	Free and Correct
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Fuel	Correct Tank, Qty
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches	Closed, Locked
Harnesses..	Secure
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency, dep. brief	Perform

Line-Up
Runway/Approach.......	Clear
Landing light, strobes	On
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Windsock.......	Check
Engine Temps and Pressures.......	Check

Normal Takeoff
Power	Full
Manifold Pressure	1-2”below ambient
Rpm	Redline

Engine parameters	Check
Rotate	60 KIAS
Climb Speed	70-90 KIAS

Airbourne with no runway left, with positive climb and above minimum retraction speed
Brakes	Apply (when airborne)
Clear of obstacles and safe climb speed
Wing Flaps	Retract
Power	Set for climb

Spin Recovery
Ailerons	NEUTRAL
Throttle	IDLE
Confirm direction
RUDDER	FULL OPPOSITE
Elevator	Forward to break stall
Rudder	Neutralise when spinning stops
Pitch	Ease out of dive

Plan to land at the nearest Airfield

EMERGENCY PROCEDURES

Right wing
Aileron	Free movement, Secure
Balance weights	Secure
Lock wires	Check, Secure
Nav Light	Check, Secure
Flaps	Check, Secure
Flap runners	Greased, correct play
Main wheel tire	Proper Inflation
Brakes	Secure, condition
Fuel tank sump	Sample
NOTE: IF after repeated sampling contamination remains report to maintenance, DO NOT Fly
Fuel Quantity	Check Visually
Fuel Filler cap	Secure

Nose
Engine oil level	Check
Fuel strainer	Sample
Propeller and spinner	Check
Alternator belt	Check
Air intake	Check
Carburetor air filter	Check
Landing lights	Check
Nose wheel strut & tire	Check
Nose-Tie down	Disconnect
Static source opening	Check

Left Wing
Aileron	Free movement, secure
Balance weights	Secure
Lock wires	Check, Secure
Nav Light	Check, Secure
Flaps	Check, Secure
Flap runners	Greased, correct play
Main wheel tire	Proper Inflation
Brakes	Secure, condition
Fuel tank sump	Sample
Fuel Quantity	Check Visually
Fuel Filler cap	Secure
Pitot Tube	Check
Stall Warning	Check
Fuel Tank Vent Opening	Check

After Start
Throttle........	....1000 rpm
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retract
Avionics Master	On
Transponder...	Standby

Taxi
Brakes...	Release, Check
Avionics	Check/Set
Flight Instruments	Check/Set
Nav instruments ....	Test
Fuel Tanks	Check

Run-up
Parking Brake	Set
Fuel Selector	Both
Engine Instruments	Green
Cowls.....	Open
Prop area	Clear
Power.......	1700 rpm
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
(150rpm drop, 50rpm differential)
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle	Idle, Check minimum rpm
Throttle	Reset 1000rpm

After Takeoff
Brakes	Check
Undercarriage	Up
Power/Pitch/Mixture	Set
Fuel	Correct tank, pump Off
Flaps	Up
Temp/Pressures	Checked
Landing Lights	OFF

Normal Climb

Airspeed	90-100 KIAS
Power	23“ and 2450RPM
Mixture	Lean above 3000ft
Cowl Flaps	Open

Cruise
Power	23", 2400RPM
Elevator and Rudder Trim	Adjust
Mixture	Lean for Cruise
Cowl Flaps	As Required
Engine Temp/Pressures	Check
Fuel	Check/Change tanks
Traffic	Check
Radio	Transmit
Estimated Times	Record

Enroute
'SAFIER'
Suction	Checked
Amps	Checked
Fuel	Checked
Icing	As Required
Engine Power/Pitch/Mixture	Set
Engine Temp/Pressures	Checked
Engine Cowl Flaps	As Required
Radios/Nav/DI	Checked and Set

Descent/Approach
'FREDALS'
Fuel	Correct Tank
Fuel Qty	Check
Radios/Nav	Set/Clearance Obtained
Engine Power/Pitch/Mixture	Set
Engine Temp/Pressures	Checked
Engine Cowl Flaps	As Required
DI	Aligned with Compass
Altimeter	Set
Landing Lights	As Required
Seats/belts, Doors	Adjusted&Locked

Approach Set Up
Flaps	Below Vfe, first stage
Brakes	Check
Undercarriage	Down
Power/Pitch/Mixture	Set
Fuel	Correct Tank
Temp/Pressures	Checked
Landing Lights	OFF
Seats/Seatbelts	Secure

Downwind Checks
Brakes	Check
Undercarriage	Down
Mixture	Set
Fuel	Correct Tank, Pumps As req'd
Temp/Pressures	Checked
Landing Lights	ON
Seats/Seatbelts	Secure

Final Approach
'CUP'
Cowls	Open
Carb Heat	Cold
Undercarriage	Down and Locked
Power/Pitch/Mixture	Set

Normal Landing
Touchdown	Main Wheels First
Nose Wheel	Lower Gently
Braking	Minimum Required

NORMAL PROCEDURES
expanded checklist
NOTE ON CHECKLISTS
A normal checklist is provided for use in flight. This checklist covers items that are of vital importance to the safety of the flight.

When completing a checklist it is assumed the pilot is familiar with the full operating procedures in the sections following the normal checklist and outlined in the aircraft POH section 4. The checklist is completed after normal flows as a cross check to ensure critical items are set correctly.

Expanded procedures for normal, non-normal, and emergency operations are provided on the reverse side. These should be used for training aids during type ratings and for personal reference.

As model differences frequently occur, the manufactures handbook for the aircraft you are flying should be referenced to prior to operation.
HAPPY FLYING!

RED SKY CHECKLISTS
Cessna 182

CONTENTS:

Preflight Inspection

START AND TAXI

PRETAKEOFF

TAKEOFF & CLIMB

CRUISE & DESCENT

APPROACHLANDING

After landing

After landing
(Once roll out complete)
Cowl Flaps	OPEN
Carb Heat	COLD
Wing Flaps	RETRACT
Transponder	Stby
Strobes/Lights	OFF

Parking
Parking Brake	SET
Time	Record
Avionics	OFF
Magnetos	Dead Cut Checked
Mixture	Cut-Off
Ignition	OFF
Master Switch	OFF
# Control Lock Installed
Paperwork	Complete

Securing the aircraft
# Control Lock Installed
Paperwork	Complete
Tie downs/covers	Installed

Compilation notes
These pages are printed front and back side, then cut around the text the first few pages need to be trimmed and bound to create a flip style checklsist with tabs at the front, and the expanded procedures on the reverse side.
  It might take a bit of time to work it out, but the result is quite effective for use by students when they are learning.

If you like jigsaw puzzles have fun!