Checklist-Piston Generic	© Red Sky Ventures 2006

CHECKLISTS BY
RED SKY VENTURES

These checklists have been developed for use in light aircraft general aviation operations.
With the exception of the run-up, these are checklists, that is checks to be completed after completion of normal cockpit actions by way of flow patterns or acronyms.

Checklists are provided in open document format to allow modification to suit your aircraft or operation. Some page formatting may be required for different page and printer settings.

The procedures in the aircraft's approved flight manual, including all applicable STCs and supplements must be followed!

NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Magnetos	Both
Master	On
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
        After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check

Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Pitch	Full fine
Flight Controls	Free and Correct
Autopilot	Off
Fuel	Correct Tank, Qty, Primer locked
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Runup....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Completed
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On
After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Retracted/Fixed
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd

Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	As Required
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs/Screens/Covers	Fitted

Abnormal maneuvers
(HASELL)
Complete prior to conducting stalls, spins and approved aerobatic maneuvers
Height	Sufficient for recovery
Above 3000ft AG
Airframe	Limitations Reviewed
Configuration Reviewed
Security	Seatbelts/Passengers/Load
Engine	Temperatures/Pressures
Power/Pitch Mixture Checked
Location	Not over built up areas,
airfields or controlled airspace High Terrain
Within proximity of suitable landing areas
Lookout	Complete a lookout turn

REFERENCE INFORMATION
Fill in for your aircraft as required
Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	____ KIAS
VX – Best Angle of Climb	____ KIAS
VY – Best Rate of Climb	Vysl _______ KIAS
Vy10,000ft_______ KIAS
Normal approach	____ KIAS
Vref	____ KIAS
VA – Maneuvering Speed	____ KIAS
PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	____KIAS
VNE – Red Line (Never Exceed)	___ KIAS

VSO – Stall landing configuration	___ KIAS
VS – Stall Clean	___ KIAS

VFE – Max. Flap Extension 10-40º	___ KIAS
VFE – Max. Flap Extension 0-10 º	___ KIAS
EMERGENCY OPERATION
Best glide Speed	___ KIAS
Slow Safe Cruise	___ KIAS
Ditching	___ KIAS
Engine failure after takeoff	___ KIAS
Engine Failure in flight flap up	___ KIAS
Engine Failure in flight flap down	____KIAS
Operating performance
Fuel Capacity (useable)	_______
Fuel Consumption Block	_______/Hr
Plan Cruise speed	___KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______
__________________	______
Loading
Maximum TO/Ldg Weight	______lbs
Standard Empty Weight	______lbs
Load limits	________
_________	________
EMERGENCIES
ENGINE FAILURE
IMMEDIATE ACTIONS
Airspeed	Best Glide
Carb Heat	ON
Field	Select
Approach	Plan
FAULT FINDING(Altitude permitting):
Carb Heat	ON
Primer	IN & Locked
Fuel Shutoff valve	ON
Mixture	RICH
Ignition	BOTH (or START)
COMMUNICATE
Mayday	Transmit on Active or 121.5
Transponder	7700
Passengers	Brief
SECURE
Mixture	cutoff
Fuel shutoff valve	off
Ignition	off
FINAL APPROACH
Flaps	as required
Master switch	Off
Doors	unlatch
Touchdown	tail low
Note: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist. It is recommended that entire engine failure during fight procedures be committed to memory
Engine Fire During Flight
Mixture	IDLE cut-off
Fuel	OFF
Master	OFF
Cabin Air	OFF
Sideslip	Initiate if required
Proceed with Engine Failure in Flight Action
Cabin Fire
Master Switch	OFF
Cabin Vents/Air/Heat	Closed
Fire Extinguisher	Activate
Cabin Vents/Windows	Open
If in flight, Once Fire is extinguished:
Electrics/Avionics	Off
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

Electrical Fire
Unknown Source
Master Switch	OFF
Avionics and Electrics	OFF
Circuit Breakers	PULL
If Smoke Ceases:
Master Switch	ON
Essential Electrical/Avionics	On, One at a time

Carburetor Icing
Carb Heat	Fully ON
Mixture	Adjust
Once icing/roughness has cleared;
Carb Heat	Cold
Mixture	Reset
Engine Roughness
Magnetos	Check
Mixture	Adjust
Temperatures/Pressures	Check
If roughness continues, plan to land at nearest suitable airfield.

NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Magnetos	Both
Master	On
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check

NORMAL CHECKLIST

Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Pitch	Full fine
Flight Controls	Free and Correct
Autopilot	Off
Fuel	Correct Tank, Qty, Primer locked
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Run-up....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Completed
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On
After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Retracted/Fixed
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d

NORMAL CHECKLIST

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached
CAUTION:
Performance and operational figures vary between models of C152, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.
REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	55 KIAS
Vto – Max performance	60KIAS
VX – Best Angle of Climb	60 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Vy10,000ft70 KIAS
Normal approach	65-75 KIAS
Vref	60 KIAS
VA – Maneuvering Speed	80-95 KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	128 KIAS
VNE – Red Line (Never Exceed)	160 KIAS

VSO – Stall landing configuration	45 KIAS
VS – Stall Clean	50 KIAS

VFE – Max. Flap Extension 0-40º	85 KIAS
EMERGENCY OPERATION
Best glide Speed	65 KIAS
Precautionary landing:
Slow Safe Cruise	80-95 KIAS
Approach (flaps full)	60 KIAS
Ditching	65 KIAS
Engine failure after takeoff	65 KIAS
Engine Failure in flight flap up	65 KIAS
Engine Failure in flight flap down	60 KIAS

Operating performance
Plan Block Consumption	40lt/hr
Plan Block Cruise speed	100KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______

NORMAL CHECKLIST

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached
CAUTION:
Performance and operational figures vary between models of C152, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.
REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	50 KIAS
Vto – Max performance	55KIAS
VX – Best Angle of Climb	55 KIAS
VY – Best Rate of Climb	Vysl 67 KIAS
Vy10,000ft63 KIAS
Normal approach	60-70 KIAS
Vref	55 KIAS
VA – Maneuvering Speed	xxxxx KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	KIAS
VNE – Red Line (Never Exceed)	KIAS

VSO – Stall landing configuration	KIAS
VS – Stall Clean	KIAS

VFE – Max. Flap Extension 0-40º	KIAS

EMERGENCY OPERATION
Best glide Speed	65 KIAS
Precautionary landing:
Slow Safe Cruise	70-85 KIAS
Approach (flaps full)	55 KIAS
Ditching	55 KIAS
Engine failure after takeoff	60 KIAS
Engine Failure in flight flap up	65 KIAS
Engine Failure in flight flap down	60 KIAS

Operating performance
Plan Block Consumption	25lt/hr
Plan Block Cruise speed	95 KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______
__________________	______
__________________	______
NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Magnetos	Both
Master	On
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check

NORMAL CHECKLIST

Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Pitch	Full fine
Flight Controls	Free and Correct
Autopilot	Off
Fuel	Correct Tank, Qty, Primer locked
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Run-up....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Completed
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On

After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Retracted/Fixed
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d

NORMAL CHECKLIST

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached
CAUTION:
Performance and operational figures vary between models of C172, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.
REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	55 KIAS
Vto – Max performance	60KIAS
VX – Best Angle of Climb	60 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Vy10,000ft70 KIAS
Normal approach	65-75 KIAS
Vref	60 KIAS
VA – Maneuvering Speed	80-95 KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	128 KIAS
VNE – Red Line (Never Exceed)	160 KIAS

VSO – Stall landing configuration	45 KIAS
VS – Stall Clean	50 KIAS

VFE – Max. Flap Extension 0-40º	85 KIAS

EMERGENCY OPERATION
Best glide Speed	65 KIAS
Precautionary landing:
Slow Safe Cruise	80-95 KIAS
Approach (flaps full)	60 KIAS
Ditching	65 KIAS
Engine failure after takeoff	65 KIAS
Engine Failure in flight flap up	65 KIAS
Engine Failure in flight flap down	60 KIAS

Operating performance
Plan Block Consumption	40lt/hr
Plan Block Cruise speed	100KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______

NORMAL CHECKLIST

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached
CAUTION:
Performance and operational figures vary between models of C172, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.
REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	55 KIAS
Vto – Max performance	60KIAS
VX – Best Angle of Climb	60 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Vy10,000ft70 KIAS
Normal approach	65-75 KIAS
Vref	60 KIAS
VA – Maneuvering Speed	80-95 KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	128 KIAS
VNE – Red Line (Never Exceed)	160 KIAS

VSO – Stall landing configuration	45 KIAS
VS – Stall Clean	50 KIAS

VFE – Max. Flap Extension 0-40º	85 KIAS

EMERGENCY OPERATION
Best glide Speed	65 KIAS
Precautionary landing:
Slow Safe Cruise	80-95 KIAS
Approach (flaps full)	60 KIAS
Ditching	65 KIAS
Engine failure after takeoff	65 KIAS
Engine Failure in flight flap up	65 KIAS
Engine Failure in flight flap down	60 KIAS

Operating performance
Plan Block Consumption	40lt/hr
Plan Block Cruise speed	100KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______
__________________	______
__________________	______
NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Circuit Breakers	Check In
Normal Engine Start
Magnetos	Both
Master	On
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check

NORMAL CHECKLIST

Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Pitch	Full fine
Flight Controls	Free and Correct
Autopilot	Off
Fuel	Correct Tank, Qty, Primer locked
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Runup....	Complete
Engine Instruments	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Completed
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On
After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Retracted/Fixed
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d
Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd

NORMAL CHECKLIST

Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine
After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached

CAUTION:
Performance and operational figures vary between models of C182, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.

REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	55 KIAS
VX – Best Angle of Climb	65 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Vy10,000ft75 KIAS
Normal approach	70-80 KIAS
Vref	65 KIAS
VA – Maneuvering Speed	90-110 KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	140 KIAS
VNE – Red Line (Never Exceed)	167 KIAS

VSO – Stall landing configuration	52 KIAS
VS – Stall Clean	58 KIAS

VFE – Max. Flap Extension 10-40º	110 KIAS
VFE – Max. Flap Extension 0-10 º	140 KIAS

EMERGENCY OPERATION
Best glide Speed	70 KIAS
Precautionary
Slow Safe Cruise	90-105 KIAS
Approach (flaps up)	70 KIAS
Approach (flaps full)	65 KIAS
Ditching	65 KIAS
Engine failure after takeoff	70 KIAS
Engine Failure in flight flap up	70 KIAS
Engine Failure in flight flap down	65 KIAS

Operating performance
Plan Block Consumption	55 lt/hr
Plan Block Cruise speed	125KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______

NORMAL CHECKLIST

Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine
After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs	Attached

CAUTION:
Performance and operational figures vary between models of C182, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.

REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	55 KIAS
VX – Best Angle of Climb	65 KIAS
VY – Best Rate of Climb	Vysl 80 KIAS
Vy10,000ft75 KIAS
Normal approach	70-80 KIAS
Vref	65 KIAS
VA – Maneuvering Speed	90-110 KIAS
Maximum demonstrated crosswind	15kts

PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	140 KIAS
VNE – Red Line (Never Exceed)	167 KIAS

VSO – Stall landing configuration	52 KIAS
VS – Stall Clean	58 KIAS

VFE – Max. Flap Extension 10-40º	110 KIAS
VFE – Max. Flap Extension 0-10 º	140 KIAS

EMERGENCY OPERATION
Best glide Speed	70 KIAS
Precautionary
Slow Safe Cruise	90-105 KIAS
Approach (flaps up)	70 KIAS
Approach (flaps full)	65 KIAS
Ditching	65 KIAS
Engine failure after takeoff	70 KIAS
Engine Failure in flight flap up	70 KIAS
Engine Failure in flight flap down	65 KIAS

Operating performance
Plan Block Consumption	55 lt/hr
Plan Block Cruise speed	125KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______
NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Magnetos	Both
Mixture....	Rich
Propeller..	High RPM
Undercarriage.	Down
Rotating Beacon....	On
Master	On
Prime.....	50-60lbs/as Required
Power......	½ Centimeter
Area.......	Clear
After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check

NORMAL CHECKLIST

Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Pitch	Full fine
Flight Controls	Free and Correct
Autopilot	Off
Fuel	Correct Tank, Qty Sufficient
Fuel Pump	Off
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Runup....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Completed
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On
After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Up, Orange Light
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Required

NOTE FOR MODELS WITH TIPTANKS:
TIP TANK Operation: Transfer from only one tip tank at a time. Ensure sufficient space is available in main tank prior to transfer (main tank should be not more than approximately half full).

NORMAL CHECKLIST

Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down, Green Light
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both

Final
Cowl Flaps	Open
Undercarriage	Down, One Green Light
Propeller Pitch	Full fine

After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Tach/Hobbs/Time	Recorded
Tie Downs	Attached

CAUTION:
Performance and operational figures vary between models of C210, refer to the aircraft's flight manual and use a fine marker pen to indicate any significant differences.

REFERENCE INFORMATION

Speeds
NORMAL OPERATION
Unless otherwise stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	70 KIAS
VX – Best Angle of Climb	80 KIAS
VY – Best Rate of Climb	Vysl 97 KIAS
Vy10,000ft93 KIAS
Normal approach	80-85 KIAS
Vref	75 KIAS
VA – Maneuvering Speed	115-135 KIAS
Maximum demonstrated crosswind	15kts
PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	195 KIAS
VNE – Red Line (Never Exceed)	165 KIAS

VS – Stall Clean	70 KIAS
VSO – Stall landing configuration	65 KIAS

VFE – Max. Flap Extn 10-30º	105 KIAS
VFE – Max. Flap Extn 0-10 º	140-165 KIAS*
VLE – Max. Gear Extension	135-165 KIAS*
VLR – Min. Gear Retraction	80 KIAS
*Speed varies significantly between models
EMERGENCY OPERATION
Best glide Speed	75-85 KIAS
Precautionary
Slow Safe Cruise	90-110 KIAS
Approach (flaps up)	85 KIAS
Approach (flaps full)	75 KIAS
Ditching	75 KIAS
Engine failure after takeoff	80 KIAS
Engine Failure in flight flap up	90 KIAS
Engine Failure in flight flap down	85 KIAS
Operating performance
Planning	65lt/hr
Plan Cruise speed	145KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______

NORMAL CHECKLIST

Before Start
Preflight Inspection	Complete
Tach/Hobbs/Time	Recorded
Passenger Briefing	Complete
Seats / Seatbelts	Adjust, Lock
Fuel Selector Valve	Both
Cowl Flaps	Open
Brakes...	Set/Hold
Avionics	Off
Electrical	Off
Circuit Breakers	Check In
Normal Engine Start
Mixture....	Rich
Propeller..	High RPM
Power......	½ Centimeter
Carburetor Heat..	Cold
Prime.....	1-3 as req’d
Rotating Beacon....	On
Area.......	Clear
        After start
Mixture....	Set for Taxi
Engine Instruments....	Check
Taxi, Nav. Lights	As Required
Flaps......	Retracted
Transponder...	Standby
Taxi
Brakes...	Release, Check
Avionics and Flight Instruments	Check/Set
Nav instruments ....	Test
Run Up
Parking Brake	Set
Fuel Selector	Both
Mixture	Set
Engine Instruments	Green
Cowls.....	Open

Power.......	Set
Mixture...	Set
Carb Heat	Check
Magnetos	Check Left, Both, Right, Both
Propeller Governor	Cycle
Engine Instruments	Check
Vacuum....	Check
Ammeter	Check with load
DI .........	Set to Compass
Throttle friction lock	Set
Idle	Check
Pre-Takeoff
Trim.......	Set for takeoff
Mixture..	Set for takeoff
Magnetos ...	Both
Propeller Governor	Full fine
Flight Controls	Free and Correct
Flaps......	Set for takeoff
Cowl Flaps ..	Open
Instruments....	Checked and Set
Radios....	Set for Departure
Navigation / GPS	Set for Departure
Hatches .	Closed, Locked
Harnesses..	Secure
Engine Runup....	Complete
Engine Instruments....	Checked
Electrics...	CB's Checked
Emergency & Dep. brief	Perform
Line Up
(REmember What To Do Last)
Runway Area.......	Clear
Engine Parameters	Green
Wind.......	Check
Transponder	Set to altitude
DI...........	Aligned with Compass, Rwy
Landing light, strobes	On

After Takeoff (above 1000' AGL)
Brakes....	Check
Undercarriage	Retracted/Fixed
Power/Pitch	Set
Mixture...	Adjust
Fuel	Checked
Flaps	Up
Engine Parameters	Green
Lights....	As required
Cruise
Power/Prop	Set
Elevator/Rudder trim	Adjust
Mixture....	Lean for altitude
Cowl Flaps	Closed/As Req’d
Descent
Fuel	Correct Tank, Qty checked
Radios	Set
Approach Briefing	Complete
Cowl Flaps	Closed
Mixture....	Set
Power/Prop	Set
Icing	As required
Lights.....	On/as req'd
Downwind
Brakes....	Check
Undercarriage	Down/Fixed
Power/Prop	Set
Mixture...	Set
Fuel	Correct Tank
Flaps	Set
Engine Parameters	Green
Lights....	As required
Seats / Seatbelts	Check Secure
Fuel Selector	Both
Carb Heat	As Required
Final
Cowl Flaps	Open
Carb Heat	Off
Undercarriage	Down & Locked/Fixed
Propeller Pitch	Full fine
After Landing
Cowl Flaps	Open
Trim.......	Takeoff
Flaps.....	Retract
Carb Heat	Off
Land, Strobe lights	Off
Transponder	Standby
Shutdown and Securing
Power.....	Idle
Avionics and Switches	Off
Mixture.......	Idle Cutoff
Mags......	Off
Master....	Off
Control Lock	In
Hobbs and Tach	Record
Tie Downs/Screens/Covers	Fitted
Briefings
Passenger Briefing:
Welcome on board, if I can have your attention for a brief you on the safety requirements and emergency equipment. Keep your seat belts fastened during flight, especially for take off and landing the seat belt is locked/fastened by........(demonstrate). The door opens/locks......... (demonstrate). There is a Crash Axe ......, a fire extinguisher......., and a first aid kit.......... (indicate positions). Should there be an emergency ensure any items that may cause damage are removed from your body and brace against the seat/glare shield, if you have any queries during the flight except during take-off or landing please ask.

Takeoff Crew Briefing:
In the event of an emergency during take-off with insufficient runway left we will select a field within 30 degrees of the runway centerline, maintain____kts, secure the aircraft and inform ATC/Traffic.
The normal departure will be with:
Takeoff power set at ___________mp/rpm,
Rotate at ____kts and climb out at ____kts,
At_________ft turn L/R to_____deg magnetic.
REFERENCE INFORMATION
Fill in for your aircraft as required
Speeds
NORMAL OPERATION
Except where stated the following speeds are for MAUW, Sea Level , ISA conditions.
VR	____ KIAS
VX – Best Angle of Climb	____ KIAS
VY – Best Rate of Climb	Vysl _______ KIAS
Vy10,000ft_______ KIAS
Normal approach	____ KIAS
Vref	____ KIAS
VA – Maneuvering Speed	____ KIAS
PLACARD/ASI LIMITATIONS
VNO – Top of Green Arc	____KIAS
VNE – Red Line (Never Exceed)	___ KIAS

VSO – Stall landing configuration	___ KIAS
VS – Stall Clean	___ KIAS

VFE – Max. Flap Extension _____º	___ KIAS
VFE – Max. Flap Extension _____º	___ KIAS
EMERGENCY OPERATION
Best glide Speed	___ KIAS
Slow Safe Cruise	___ KIAS
Ditching	___ KIAS
Engine failure after takeoff	___ KIAS
Engine Failure in flight flap up	___ KIAS
Engine Failure in flight flap down	____KIAS
Operating performance
Fuel Capacity (usable)	__________
Fuel Consumption Block	_______/Hr
Plan Cruise speed	_____KTAS
Other Information
Transponder Codes:
Unlawful Interference	7500
Loss of Communication	7600
Emergency	7700
Unassigned	2000
Radio Frequencies
Emergency Frequencies	121.5/243
__________________	______
__________________	______
__________________	______
__________________	______
Loading
Maximum TO/Ldg Weight	______lbs
Standard Empty Weight	______lbs
Load limits	________
_________	________
Signals

Signal	On Ground	In Flight
Green Steady	Takeoff	Land
Green Flashing	Taxi	Return to land
Red Steady	Stop	Give way
Red Flashing	Clear runway	Do not land
White Flashing	Return to ramp	--
Red/Green Alternating	WARNING – use Caution

EMERGENCY PROCEDURES
Engine failure
TAKEOFF
NOTE: Bold Items are immediate recall Items, other times may be followed up by the use of the AFM checklist.
Throttle	IDLE
Brakes	Apply
Flaps	UP
Mixture	IDLE cut-off
Ignition	OFF
Master switch	OFF
AFTER TAKEOFF
Airspeed	___KIAS Flaps Up
____KIAS Flaps Down
Mixture	Idle Cut-off
Fuel shutoff valve	OFF
Ignition	OFF
Flaps	as required
Master switch	OFF
DURING FLIGHT
IMMEDIATE ACTIONS
Airspeed	Recommended Speed
Carb Heat	ON
Field	Select
Approach	Plan
FAULT FINDING
Carb Heat	ON
Primer	IN & Locked
Fuel Shutoff valve	ON
Mixture	RICH
Ignition	BOTH (or START)
COMMUNICATE
Mayday	Transmit Active or 121.5
Transponder	7700
Passengers	Brief
SECURE
Mixture	cutoff
Fuel shutoff valve	off
Ignition	off
FINAL
Flaps	as required
Master switch	Off
Doors	unlatch
Touchdown	tail low
Engine Fire
during start
Starter	Crank
To draw away flames, If Engine Starts:
Power	1700rpm
For a few minutes until flames appear to be extinguished, or if engine does not start:
Mixture	IDLE cut-off
Ignition	OFF
Master	OFF
Inspect damage
during flight
Mixture	IDLE cut-off
Fuel	OFF
Master	OFF
Cabin Air	OFF
Sideslip	Initiate if required
Proceed with Engine Failure in Flight Actions
Cabin Fire
On the Ground
Master Switch	OFF
Cabin Vents/Air/Heat	Closed
Fire Extinguisher	Activate
Cabin Vents/Windows	Open

During flight
Follow Above Procedure, Once Fire is extinguished:
Electrics/Avionics	Off
Master	ON
Avionics/Electrics	On, one at a time
Land at the nearest Suitable Airfield

Electrical Fire
Unknown Source
Master Switch	OFF
Avionics and Electrics	OFF
Circuit Brekers	PULL
If Smoke Ceases:
Master Switch	ON
Essential Electrical/Avionics	On, One at a time
Electrical failure/Overload
Load	verify
Reduce to minimum
Alternator	OFF
Alternator CB	Trip&Reset
Alternator	ON
Load/Power	OK?
If Not:
Master	OFF
Master	ON
IF LOAD still not does not return to normal: PLAN To land at nearest suitable airfield,
Conserve Battery as much as possible,
All non essential electrics off, if necessary Inform ATC and turn master off until approaching circuit.
Be prepared for implications of electrical failures on systems(flaps/gear)
Carburetor Icing
Carb Heat	Fully ON
Mixture	Adjust
Once icing/roughness has cleared;
Carb Heat	Cold
Mixture	Reset
Engine Roughness
Magnetos	Check
Mixture	Adjust
Temperatures/Pressures	Check
If roughness continues, plan to land at nerest suitable airfield.
Spin Recovery
Ailerons	NEUTRAL
Throttle	IDLE
Confirm direction
RUDDER	FULL OPPOSITE
Elevator	Forward to break stall
Rudder	Neutralise when spinning stops
Pitch	Ease out of dive

ABNORMAL PROCEDURES

Short field take-off
Wing Flaps	Takeoff
Brakes	APPLY
Power	Maximum
Mixture	Set for Field Elevation
Brakes	RELEASE
Elevator Control	Slightly Tail Low Climb Speed	Vx______kts
Accelerate	Vy______kts
Wing Flaps	RETRACT
Power	Set for climb

Note: Do not reduce power until wing flaps and landing gear have been retracted.
Soft field take-off
Wing Flaps	Maximum for field
Line up	Do not stop rolling
Takeoff roll	Nose high
Liftoff	Minimum speed
After Takeoff	Accelerate Vx/Vy As req'd

Crosswind take-off
Wing Flaps	Minimum for field
Takeoff roll	Ailerons Into wind
Liftoff	Ailerons Neutral
After takeoff	Crab into wind for drift
Maximum Performance Climb
Wing Flaps	Up
Power	Maximum Climb
Pitch	Maximum Continuous
Note: for an after takeoff climb or in an emergency full power may be used, for normal operations ensure time limits are not exceeded
Mixture	Set for Field Elevation
Airspeed	Vysl _______KIAS (sea level)
Vy10,000 ____ KIAS (10,000ft)
Cowl Flaps	Open
Note: Vy will provide maximum rate of climb, when performance is limiting such that less than 200fpm is achieved, the reduction to best angle of climb may result in zero or negative rate of climb.
Short field landing
Flaps	Full
Airspeed	___kts
Touchdown Positive, Main Wheels First
Nose Wheel	Lower
Braking	Maximum Steady Braking
Flaps	Retract
Soft field landing
Flaps	Full
Airspeed	____kts
Touchdown,	Softly Main Wheels First
Nose Wheel	Lower gently
Elevator	Full up
Braking	Gently, minimum required
Flaps	Leave down until clear of rwy
Crosswind landing
Wing Flaps	minimum for field length
(and as required by strength of wind)
Approach	crab into wind
Touchdown Nose straight, on into wind wheel
After landing	Ailerons into wind
Go-around
Mixture/Pitch/Throttle	Forward
Wing Flaps	Retract to Takeoff
Brakes	APPLY
Once a Positive Climb is achieved and above Vlr:
Landing Gear	RETRACT
After obstacles are cleared and above Vx:
 Wing Flaps	RETRACT
Power	Set for climb
Note: Do not reduce power until wing flaps and landing gear have been retracted.
Abnormal Maneuvers
Height	Sufficient for recovery
Above 3000ft AG
HASELL : Complete prior to conducting stalls, spins and approved aerobatic maneuvers
Airframe	Limitations Reviewed
Configuration Reviewed
Security	Seatbelts/Passengers/Load
Engine	Temperatures/Pressures
Power/Pitch Mixture Checked
Location	Not over built up areas,
airfields or controlled airspace High Terrain
Within proximity of suitable landing areas
Lookout	Complete a lookout turn