Fuel Planning

Date: / /		Reg.

Cessna 210/206

## Fuel Planning
		FUEL LITRES
ENROUTE TIME @ 60 LITRES / HOUR
10 % CONTINGENCY FUEL
RESERVE (45 MINS) @ 60 LITRES / HOUR		45 litres
TAXI / TAKEOFF
UNUSABLE FUEL
	MIN FUEL REQUIRED
	TOTAL FUEL DIPPED

LESS UNUSABLE FUEL	(Included in aircraft empty weight)	-

Litres to pounds		« x 1.584
TOTAL FUEL WEIGHT TO WEIGHT AND BALANCE SHEET

Weight & Balance Loading Sheet

ITEM	WEIGHT	ARM	MOMENT / 1000

Aircraft Empty Weight (Flt. Docs)
Pilot, front passenger
Centre Passenger(s)
Rear Passenger(s)
Baggage Area 1 (Max ____ lbs)
Baggage Area 2 (Max ____ lbs)
Fuel Weight 1 (Max ____ lbs)
Fuel Weight 2 (Max ____ lbs)
Other
Initial Takeoff Weight / (Max _____ lbs)
+/- Additional FUEL Adjustment
FINAL TAKEOFF WEIGHT / (Max _____ lbs)
Less Fuel Burn
LANDING WEIGHT / (Max ______ lbs)

Weight x Arm = Moment.
Total Moment = Sum of all Moments (+ or -)
Total Weight = Sum of all Weights (+ or -)
Final C. of G. = Total moment / Total weight

Departure Performance
Departure AIRFIELD					GROUP RATING
VARIATION				AIRCRAFT GROUP RATING
I.S.A.		1013					+15
LESS QNH				-Press alt/1000x2
DIFFERENCE				-AMBIENT TEMPERATURE
		x 30 feet					x 120 feet

Plus ELEVATION				Plus ELEVATION
=PRESSURE ALTITUDE				=DENSITY ALTITUDE
wind TRUE		+/- VARIATION					= WIND MAGNETIC
				RUNWAY HEADING
				ANGULAR DIFFERENCE
CROSS WIND COMPONENT				HEADWIND COMPONENT
MAX DEMONSTRATED
SLOPE					Nil sig
SURFACE					paved
Take off roll required

TOTAL TAKEOFF DISTANCE REQUIRED
TAKEOFF DISTANCE AVAILABLE

Arrival Performance
ARRIVAL AIRFIELD					GROUP RATING

VARIATION					AIRCRAFT GROUP RATING

				airfield elevation

Wind TRUE		+WEST/-EAST / VARIATION					= WIND MAGNETIC
				RUNWAY HEADING
				ANGULAR DIFFERENCE

CROSS WIND COMPONENT					HEADWIND COMPONENT
MAX DEMONSTRATED
				SLOPE

SURFACE

LANDING ROLL REQUIRED
LANDING DISTANCE REQUIRED

LANDING DISTANCE AVAILABLE

Navigation Calculation Work Sheet

FM	TO	FL	Temp	W/V	IAS	TAS	DRIFT	Hdg T	VAR.	Hdg M	G/S	Dist	EET

TOTALS

In-Flight Log

FM	TO	FL	TRK / True	W/V	HDG / True	HDG / Mag	Dist	G/S	EET	ETA1	ETA2	ETA3	ATA

TOTALS

FUEL LOG
LEFT TANK			RIGHT TANK
TIME ON	FUEL USED	REMAINING	TIME ON	FUEL USED	REMAINING